## Slide 1: Abstract
High-throughput and adaptive feedback microscopy
Christian Tischer, Sabine Reither, Volker Hilsenstein, Beate Neumann, Rainer Pepperkok
Advanced Light Microscopy Facility, EMBL Heidelberg
Meyerhofstr.1, 69117 Heidelberg, Germany
High-throughput microscopy of siRNA treated cells has become a standard tool for discovering genes with roles in specific biological processes. However, conducting high-throughput microscopy experiments is still challenging as it puts high demands on sample preparation, microscopy, image and data analysis. Moreover, further characterization of the “hit genes” often requires demanding microscopic assays that are difficult to perform even in medium throughput. In this talk, I will outline the typical challenges occurring in high-throughput microscopy and discuss how dedicated microscope systems can help to tackle these challenges. In addition, I will describe how “adaptive feedback microscopy” allows scientist to perform highly complex microscopic assays in a fully automated manner, thereby enabling detailed and systematic further investigation of the identified “hit genes”.

## Slide 2: To do
Name of cel

## Slide 3: High-throughput and adaptive feedback microscopy
Christian Tischer, Sabine Reither, Volker Hilsenstein, Beate Neumann, Rainer Pepperkok
Advanced Light Microscopy Facility, EMBL Heidelberg
Meyerhofstr.1, 69117 Heidelberg, Germany

## Slide 5
Biological process
Protein localization dynamics
Which proteins?
Protein-protein
interaction dynamics
High-throughput screening microscopy
“Primary” screen
Protein knockdown by siRNA
Monitor perturbation of biological process in microscopy assay
“Secondary” screen
“Secondary” screen
Notes: You have an assay that tells you whether the process of interest is working and then you look in the presence of siRNAs whether the process is still working.

## Slide 6: Temperature stability

## Slide 7: Cost efficiency
Fig. 2: Double colour imaging in plastic cell culture plates.
HeLa-Kyoto cell stably expressing H2B-mcherry and GFP-tubulin were cultured in a
plastic cell culture plate from NUNC, fixed and subsequently imaged using a 20x/0.75NA
objective with a magnification changer 2. (A,D) GFP-tubulin, (B,E) H2B-mcherry, (C,F)
overlay image (GFP-tubulin shown in green and H2B-mcherry in red). Scale bar 10 μm.
Interphase
Mitosis
GFP-Tubulin
Merge
DNA (Hb2-mCherry)

## Slide 8: Edge effects

## Slide 9: Autofocus CellDiscoverer 7
Find Surface
Focus Hold
Focus every time-point and position

## Slide 10: Speed
Filter wheel vs. other
=>Sabine, Speed Mdev?

## Slide 11: Variable NA imaging

## Slide 12: Autophagosome screen
Treatment A
Treatment B
In principle, the total intensity inside all dot-like structures
in each cell is proportional to the amount of protein recruited
to autophagosomes in this cell.

## Slide 13: Acquisition modalities
CCD
z
10 micrometer
PMT
CCD
Confocal NA1.4
Widefield NA0.9
Widefield NA0.3

## Slide 14: Low NA imaging of thin samples in wide-field microscopes
NA 0.9
NA 0.3
x
z
x
y
HeLa cell, Golgi-GFP
dz = 1 micrometer
NA 0.8
NA 0.26
z
NA 0.35

## Slide 15: Low NA Transmission
Sebastian!

## Slide 16: What to measure
Mean vs Sum
Cell cycle example

## Slide 17: Secondary Screens

## Slide 18: What to measure
Mean vs Sum
Cell cycle example

## Slide 19: Intelligent Microscopy [Conrad et al.] Adaptive Feedback Microscopy [Tischer et al.] Smart Microscopy [Huisken et al.] Open Application Development (OAD) [Zeiss]
Todo:
replace where possible with icons
add references
Look for more synonyms

## Slide 20: High-resolution Adaptive Feedback Time-lapse Imaging of Mitosis
- Move to next grid position. - Acquire low-zoom, single plane, single channel image
Data: H2B-mCherry
Todo:
make images gray-scale
Add microscope icon
Automated analysis:
Mitotic cell coordinates
x=150 y=80
Microscope:
- Move to x,y - Acquire high-zoom, multi plane, dual color, time lapse data
x, y

## Slide 21: Adaptive Feedback Microscopy using ZEISS products
Microscope Examples | Zeiss Software | Open Application Development Modality | Image Analysis Modalities
LSM510 confocal (1) LSM780 confocal LSM880 confocal | ZEN Black | Visual Basic scripting with macro recording | Visual Basic or external software
LSM800 confocal CellDiscoverer 7 widefield | ZEN Blue | Python scripting with macro recording | ZEN Blue interal image analysis or external software
(1) Rabut and Ellenberg, Automatic real-time three-dimensional cell tracking by fluorescence microscopy. J. Microscopy, 2004

## Slide 22
Zeiss
LSM780
Visual Basic
ImageJ Analysis
Multi-step Adaptive FRAP Microscopy
In this way several hundreds of recovery data sets can be automatically acquired in an overnight experiment, thus drastically increasing the data significance
compared to manual data acquisition where at best several tens of useful datasets
can be acquired in the same amount of time.

## Slide 23: Adaptive FCS Microscopy

## Slide 27: Image analysis, quality control and statistics

## Slide 28
Acknowledgements
ALMF team:
Beate Neumann
Sabine Reither
Volker Hilsenstein
Yury Belyaev
Stefan Terjung
ALMF alumni
Christian Conrad
Jutta Bulkescher
FCS:
Malte Wachsmuth
Frank Sieckmann (Leica)
Zeiss LSM780 automation:
Gwen Rabut, Annelie Wuensche, Antonio Politi
Jan Ellenberg
Rainer Pepperkok
Green: actin cytoskeleton
Red: nucleus
Cells treated with PDGF