## Slide 1: High-throughput and Adaptive Feedback Microscopy
Christian Tischer, Sabine Reither, Volker Hilsenstein, Beate Neumann, Rainer Pepperkok
Advanced Light Microscopy Facility, EMBL Heidelberg
Meyerhofstr.1, 69117 Heidelberg, Germany
High-throughput microscopy of siRNA treated cells has become a standard tool for discovering genes with roles in specific biological processes. However, conducting high-throughput microscopy experiments is still challenging as it puts high demands on sample preparation, microscopy, image and data analysis. Moreover, further characterization of the “hit genes” often requires demanding microscopic assays that are difficult to perform even in medium throughput. In this talk, I will outline the typical challenges occurring in high-throughput microscopy and discuss how dedicated microscope systems can help to tackle these challenges. In addition, I will describe how “adaptive feedback microscopy” allows scientist to perform highly complex microscopic assays in a fully automated manner, thereby enabling detailed and systematic further investigation of the identified “hit genes”.

## Slide 2: This ‘tech-talk’ is for…
…biological scientists considering conducting high-throughput microscopy experiments and are looking for technical advice advice what to pay attention to in terms of
Microscope system
Assay development
Data analysis

## Slide 3
Advanced Light Microscopy Facility (ALMF) at EMBL Heidelberg, Germany
Advanced Light Microscopy Facility
High-Throughput Microscopy
Rainer Pepperkok
Christian Tischer
Beate Neumann
Stefan Terjung
Volker Hilsenstein
Marko Lampe
Head of Facility
Sabine Reither
Aliaksandr Halavatyi
Tobias Rasse
Around 30 microscope systems
Since 1998 serving EMBL scientists and international visitors

## Slide 4
Current Industrial Partners (in alphabetical order)
This talk

## Slide 5: A ‘typical’ HT-microscopy experiment
Biological process
Find novel genes
Bioinformatic filter
~500 putative genes
~1500 siRNAs (3 per gene)
~54 96-well plates (3 replicates)
~40000 images
20x lens
2 channels
4 positions per well
Image analysis of
~4 million cells
Few “hit” genes
?
!
Statistics

## Slide 6
Completed HT-microscopy projects with ALMF support
Protein secretion / membrane
trafficking / organelle organisation
Simpson et al., Nat Cell Biol. 2012
DNA repair
Gudjonsson et al., Cell 2012
Lukas et al., Nat Cell Biol. 2011
Doyle et al., Cell. 2009
Plasma membrane targeting
Ritzerfeld et al., Genome Research 2011
Neumann et al., Nature 2010
Cell division
Cholesterol metabolism
Cystic Fibrosis
Almaca et al., Cell 2013
Bartz et al, Cell Metab. 2009
Blattmann et al., PloS Genet 2013
Boni et al. J Cell Biol 2015
Inner membrane nuclear targeting
Notes: RNAi microarrays are Here you can see the summary of projects using RNAi microarrays.
All projects labelled in red were genome-wide screens.
These RNAi microarrays can be used for many different assays types as shown here.

## Slide 7: Microscope system considerations

## Slide 8: Multi-color Imaging Modalities
Filter cube
>100 ms
Halogen
lamp
Emission filter wheel >10 ms
LED
~ 1 ms
Multi-band dichroic
Multi-band emission filter
Multi-band dichroic
Crosstalk?!
Faster, no crosstalk
LED
~ 1 ms
Simultaneous imaging using multi-camera solutions….
$$
~100ms
~100ms
~100ms

## Slide 9: Auto-focus modalities
“Software” autofocus
Multiple pre-images of the sample
to find best (highest contrast) plane
Pro:
Can deal with samples at different z-positions
Con:
Slow (>>1s)
Not good for sample
Can get confused if objects are in multiple planes
“Hardware” autofocus
Finds coverslip surface based on reflection of (far-red) light
Pro:
Faster (<1s)
Better for sample
Con:
Requires constant sample z-position
Requires presence of reflective surface
fixed offset

## Slide 10: Environmental control
37C ?!
37C ?!
37C ?!
Zeiss CellDiscoverer 7, H2B-mCherry
10x every 30min, 48h
38C => visible mitotic defects
(e.g., increased mitotic index and micro-nuclei formation)
Cropped and enlarged view on above movie

## Slide 11: Sample mounting
Interphase
Mitosis
GFP-Tubulin
Merge
Hb2-mCherry
Zeiss CellObserver 7, 40x magnification, NA0.7
Imaged through 1mm plastic bottom
Plate bottom | Cell growth | Price | Imaging quality
Plastic | + | ~2 $ | o,+
Glass | o | ~10 $ | ++

## Slide 12: Multi-well Transmission Imaging
Condenser lens
!
Brightfield contrast
“Phase gradient contrast”
Zeiss CellDiscoverer 7, 5x magnification
!

## Slide 13: Assay development considerations

## Slide 14: Autophagosome screen
Treatment A
Treatment B
In principle, the total intensity inside all dot-like structures
in each cell is proportional to the amount of protein recruited
to autophagosomes in this cell.

## Slide 15: Acquisition modalities

## Slide 16: Confocal stacks
z
10 um
Point scanning confocal
Spinning disc confocal
on-the-fly sum projection?!
Typically too slow
Quite fast (>=1s per stack)
but 3-D data
and 3-D analysis
10x less data, simpler 2D analysis

## Slide 17: Widefield stack with high NA lens
Widefield NA0.9
(on-the-fly) deconvolution and sum projection
Sum projection
z-stack, dz=1 um
Sum projection after widefield-deconvolution
Morphology: ok
Intensities: ?
Zeiss CellDiscoverer 7 Golgi-GFP, cropped image
10 um

## Slide 18: Wide-field single plane with low NA lens
NA 0.9
NA 0.3
Zeiss CellDiscoverer 7 (adaptable NA)
Hela cell, Golgi-GFP
NA 0.8
80 ms
30% light
NA 0.26
380 ms
80% light
NA 0.35
150 ms
40% light
z
Widefield NA0.3
Whole cell in focus in one single image
z-stack
1um steps
Central plane

## Slide 19: Image analysis, quality control and statistics

## Slide 20: Image analysis, Visual inspection and Statistics
+
+
Gene
Hit
List
+
Image analysis
Visual inspection
Statistics
Integrated solution from one company
Pro:
Least IT hassle
Turn-key solutions for some standard assays
Con:
If, e.g., a specific image analysis or statistics module is missing it might be difficult to add

## Slide 21: Image analysis, Visual inspection and Statistics
Linux Compute Cluster
20000 image sets
=> 1000 parallel jobs
20 image sets per job
1h min total analysis time
+
+
.tif images, defined naming scheme
Mol. Devices
Leica
Nikon
Olympus
File conversion and renaming
“Raw” images, central storage
Segmentation images
+ Table (txt file)
Simple Laptop
‘HTM-Explorer’ R and ImageJ
Gene
Hit
List
+

## Slide 22: List of interesting genes … and now?
Most interesting gene => PhD project
Bio-informatic network analysis
High-content ‘secondary’ screens
Protein localization dynamics
  High-resolution time-lapse
  Fluorescence recovery after photo-bleaching (FRAP)
Protein mobility and interactions
  Fluorescence cross correlation spectroscopy (FCS)

## Slide 23: Intelligent Microscopy Adaptive Feedback Microscopy Smart Microscopy Open Application Development (OAD) [Zeiss]
Todo:
add references
Look for more synonyms
Adapted settings
Analyze data
Conrad et al., Nature Methods (2011)
Tischer et al., Methods Cell Biol. (2014)
Scherf & Huisken, Nature Biotechnology (2015)

## Slide 24: High-resolution Adaptive Feedback Time-lapse Imaging of Mitosis
Move to pre-defined position
Acquire low-res image
x=150 y=80
Zoom in on target object
Acquire high-content data
x, y
H2B-mCherry
single plane
Find mitotic cell

## Slide 25
Todo:
add references
Look for more synonyms
Zeiss ZEN Blue (e.g., LSM 800, CellDiscoverer 7)
Python Programming Interface
ImageJ
CellProfiler
CellCognition
Zen Blue Image Analysis Modules

## Slide 26
Todo:
add references
Look for more synonyms
Zeiss AIM (LSM 510)
Zeiss ZEN Black (e.g., LSM 780, LSM 880)
Visual Basic Programming Interface
[1] Rabut and Ellenberg, Automatic real-time three-dimensional cell tracking by fluorescence microscopy. J. Microscopy, 2004
ImageJ
CellProfiler
CellCognition
Custom written visual basic
“Pipeline constructor” [1]
(Antonio Politi, Jan Ellenberg)

## Slide 27
Adaptive FRAP Microscopy
Hundreds of experiments fully automated over night
Aliaksandr Halavatyi (EMBL Heidelberg)
Zeiss LSM780
Visual Basic
ImageJ
Move to next grid position
Tischer et al., Adaptive Feedback Microscopy (2014) Methods in Cell Biology
Halavatyi et al., High-throughput Microscopy (2016) GIT Imaging and Microscopy

## Slide 28
Adaptive FCCS Microscopy

## Slide 29: Need for Automated Immersion System
FRAP and FCS => high NA => Immersion Lenses
~ 13 cm
96-well imaging plate
Automated immersion (oil and water)

## Slide 30
Acknowledgements
ALMF team:
Beate Neumann
Sabine Reither
Volker Hilsenstein
Aliaksandr Halavatyi
Tobias Rassse
Stefan Terjung
Rainer Pepperkok
Ellenberg Team:
Antonio Politi
Jan Ellenberg
Zeiss for the invitation to give this talk!
Green: actin cytoskeleton
Red: nucleus
Cells treated with PDGF

## Slide 32: What to measure
Mean vs Sum
Cell cycle example

## Slide 33
Autofocus on Histone 2B-mCherry
Find suitable cell:
- Nuclear shape
- Fluorescence levels
Generate coordinates
- 3 inside nucleus
- 3 inside cytplasm
For each coordinate acquire 30s FCS
Move to next position
Image
H2B-mCherry
Protein-YFP
Report to microscope:
- Object coordinates
- Laser intensity
- Exposure time
- …
Microscopy automation for FCS on chromatin binding factors
Notify analysis software:
- path to images
{x,y}
Leica Sp5 & FCCS
(CAM Interface)
Micropilot
I(t)
t
HeLa cells stably expressing Histone2B-mCherry; transiently expressing different EYFP constructs
Malte Wachsmuth, Ellenberg Lab, EMBL HD
Notes: Say:
For this project they were interested to find out whether proteins are interacting with Chromatin!
So they used a cell line stably expressing Histone 2B-mCherry which is bound to chromatin and co-expressed other YFP-tagged proteins
For this we used…
Malte:
- Autofocus on cells?
- Image of this?
What is the plate layout?
How do you do the transfection?
MicroPilot reports back the location of several cells in one image?
What are the cell selection criteria? Nuclear shape and GFP signal intensity?
It is Leica SP5 with Picoquant FCCS, right?
Can one also say Histone2B instead of H2B?
If you see a crosscorrelation with H2B-mCherry, what is the conclusion?
  Direct Interaction with H2B-mCherry
  Indirect Interaction due to Chromatin binding? (they wobble together on the DNA)
  If both is possible, can we distinguish?
The fast Diffusion Coefficient of GATA3 and H2A is that in accordance with their size?

## Slide 34
D1 = 29.8 ± 0.2 µm2s-1
f2 = no significant 2nd component
CC = 1.02 ± 0.06%
(2172 measurements in 979 cells)
EYFP
H2B-mCherry
Automated FCCS on protein-chromatin interaction (3 examples from currently 53)
EYFP:
Only free diffusive
H2A-EYFP
H2B-mCherry
D1 = 7.2 ± 0.5 µm2s-
D2 = 0.28 ± 0.02 µm2s-1 , f2 = 24 ± 1%
CC = 44 ± 2%
(137 measurements in 74 cells)
Histone 2A:
Free and bound fraction
Chromatin interaction
GATA3-EYFP
H2B-mCherry
D1 = 4.2 ± 0.5 µm2s-1
D2 = 0.19 ± 0.01 µm2s-1 , f2 = 35 ± 3%
CC = 18 ± 2%
(137 measurements in 74 cells)
GATA3 (transcription factor):
Free and bound fraction
Chromatin interaction
Malte Wachsmuth, Ellenberg Lab
Notes: So far we imaged 53 constructs and here i show you 3 examples

## Slide 35: Adaptive FCS Microscopy

## Slide 36
Biological process
Protein localization dynamics
Which proteins?
Protein-protein
Interaction dynamics
High-throughput Screening Microscopy
“Primary” screen
Protein knockdown by siRNA
Monitor perturbation of biological process in microscopy assay
“Secondary” screen
“Secondary” screen
Notes: You have an assay that tells you whether the process of interest is working and then you look in the presence of siRNAs whether the process is still working.

## Slide 37: Low NA Transmission Imaging
Image without shadows
Image without shadows
Condenser Aperture
Celldiscoverer 7
logo

## Slide 38: Adaptive Feedback Microscopy using ZEISS products
Microscope Examples | Zeiss Software | Open Application Development Modality | Image Analysis Modalities
LSM510 confocal (1) LSM780 confocal LSM880 confocal | ZEN Black | Visual Basic scripting with macro recording | Visual Basic or external software
LSM800 confocal CellDiscoverer 7 widefield | ZEN Blue | Python scripting with macro recording | ZEN Blue interal image analysis or external software
(1) Rabut and Ellenberg, Automatic real-time three-dimensional cell tracking by fluorescence microscopy. J. Microscopy, 2004