## Slide 1: High-throughput and Adaptive Feedback Microscopy
Christian Tischer, Sabine Reither, Volker Hilsenstein, Beate Neumann, Rainer Pepperkok
Advanced Light Microscopy Facility, EMBL Heidelberg
Meyerhofstr.1, 69117 Heidelberg, Germany
High-throughput microscopy of siRNA treated cells has become a standard tool for discovering genes with roles in specific biological processes. However, conducting high-throughput microscopy experiments is still challenging as it puts high demands on sample preparation, microscopy, image and data analysis. Moreover, further characterization of the “hit genes” often requires demanding microscopic assays that are difficult to perform even in medium throughput. In this talk, I will outline the typical challenges occurring in high-throughput microscopy and discuss how dedicated microscope systems can help to tackle these challenges. In addition, I will describe how “adaptive feedback microscopy” allows scientist to perform highly complex microscopic assays in a fully automated manner, thereby enabling detailed and systematic further investigation of the identified “hit genes”.

## Slide 2: Advanced Light Microscopy Facility (ALMF) at EMBL Heidelberg
Headed by Rainer Pepperkok
Around 30 microscope systems
Since Serving EMBL scientists and world-wide visitors.

## Slide 3
Biological process
Protein localization dynamics
Which proteins?
Protein-protein
Interaction dynamics
High-throughput Screening Microscopy
“Primary” screen
Protein knockdown by siRNA
Monitor perturbation of biological process in microscopy assay
“Secondary” screen
“Secondary” screen
Notes: You have an assay that tells you whether the process of interest is working and then you look in the presence of siRNAs whether the process is still working.

## Slide 4: HTM Screening Projects at ALMF
Name Project List with Picturescel

## Slide 5: Things you may pay attention to when acquiring a new high-throughput screening system

## Slide 6: Multi-color Imaging Modalities
Sample
Filter cubes
hundreds of milliseconds
Halogen light source
fixed
Sample
Emission filter wheel tens of milliseconds
LED
Switching
milliseconds
Multi-band dichroic fixed
Sample
Multi-band emission filter
fixed
LED
Switching
milliseconds
Multi-band dichroic fixed
Fastest, but potential crosstalk
Faster, no crosstalk
Slowest, no crosstalk

## Slide 7: Auto-focus modalities
“Software” autofocus
“Hardware” autofocus

## Slide 8: Temperature stability
Add movie

## Slide 9: Running costs
Fig. 2: Double colour imaging in plastic cell culture plates.
HeLa-Kyoto cell stably expressing H2B-mcherry and GFP-tubulin were cultured in a
plastic cell culture plate from NUNC, fixed and subsequently imaged using a 20x/0.75NA
objective with a magnification changer 2. (A,D) GFP-tubulin, (B,E) H2B-mcherry, (C,F)
overlay image (GFP-tubulin shown in green and H2B-mcherry in red). Scale bar 10 μm.
Interphase
Mitosis
GFP-Tubulin
Merge
DNA (Hb2-mCherry)
Celldiscoverer 7
logo
Picture multi-well plate
Prices for glass-bottom
And plastic-bottom
Todo: check effective NA=40x/0.75?
$$$

## Slide 10: Things to pay attention to when acquiring a new high-throughput screening system

## Slide 11: Things to pay attention to when acquiring a new high-throughput screening system

## Slide 12: Things to pay attention to when acquiring a new high-throughput screening system

## Slide 13: Things to pay attention to when acquiring a new high-throughput screening system

## Slide 14: Edge effects

## Slide 15: Autofocus CellDiscoverer 7
Find Surface
Focus Hold
Focus every time-point and position

## Slide 16: Autophagosome screen
Treatment A
Treatment B
In principle, the total intensity inside all dot-like structures
in each cell is proportional to the amount of protein recruited
to autophagosomes in this cell.

## Slide 17: Acquisition modalities: confocal
z
10 micrometer
Z-stack with point scanning confocal
Z-stack with spinning disc confocal
Good option, if available: on-the-fly z sum projection during acquisition
  Save ~10x disc space
  Simplify image analysis workflow (2-D only)
Typically too slow for high-throughput screening

## Slide 18: Acquisition Modalities: Widefield
Widefield NA0.9
Widefield NA0.3
Good option, if available: on-the-fly deconvolution and z sum projection during acquisition
  Save ~10x disc space
  Greatly simplify image analysis workflow (2-D only, no deconvolution)

## Slide 19: Low NA Fluorescence Imaging
NA 0.9
NA 0.3
x
z
x
y
HeLa cell, Golgi-GFP
dz = 1 micrometer
NA 0.8
NA 0.26
z
NA 0.35
Celldiscoverer 7
logo

## Slide 20: Advice
High-throughput screening microscopy is not about pretty 3-D pictures but about fast and manageable measurements.
Typical: 100x Oil lens confocal z-stacks => Single plane 20x Air lens

## Slide 21: Multi-well Transmission Imaging
Image with shadows
Image without shadows

## Slide 22: Low NA Transmission Imaging
Image without shadows
Image without shadows
Condenser Aperture
Celldiscoverer 7
logo

## Slide 23: What to measure
Mean vs Sum
Cell cycle example

## Slide 24: Secondary Screens

## Slide 25: What to measure
Mean vs Sum
Cell cycle example

## Slide 26: Intelligent Microscopy [Conrad et al.] Adaptive Feedback Microscopy [Tischer et al.] Smart Microscopy [Huisken et al.] Open Application Development (OAD) [Zeiss]
Todo:
add references
Look for more synonyms
Sent new microscope settings
Analyze data to derive adapted microscope settings

## Slide 27: High-resolution Adaptive Feedback Time-lapse Imaging of Mitosis
- Move to next grid position. - Acquire low-zoom, single plane, single channel image
Todo:
make images gray-scale
Add microscope icon
Automated analysis:
Mitotic cell coordinates
x=150 y=80
Microscope:
- Move to x,y - Acquire high-zoom, multi plane, dual color, time lapse data
x, y

## Slide 28
Todo:
add references
Look for more synonyms
ZEN Black
Logo, LSM510 logo
(1) Rabut and Ellenberg, Automatic real-time three-dimensional cell tracking by fluorescence microscopy. J. Microscopy, 2004

## Slide 29
Todo:
add references
Look for more synonyms
ZEN Blue
(1) Rabut and Ellenberg, Automatic real-time three-dimensional cell tracking by fluorescence microscopy. J. Microscopy, 2004
ZEN Blue

## Slide 30
Zeiss
LSM780
Visual Basic
ImageJ Analysis
Multi-step Adaptive FRAP Microscopy
In this way several hundreds of recovery data sets can be automatically acquired in an overnight experiment, thus drastically increasing the data significance
compared to manual data acquisition where at best several tens of useful datasets
can be acquired in the same amount of time.

## Slide 31: Adaptive FCS Microscopy

## Slide 32: Automated Immersion System
Both FRAP and FCS typically require high NA imaging => Objective Lenses with Immersion

## Slide 33: Image analysis, quality control and statistics

## Slide 35
Acknowledgements
ALMF team:
Beate Neumann
Sabine Reither
Volker Hilsenstein
Yury Belyaev
Stefan Terjung
ALMF alumni
Christian Conrad
Jutta Bulkescher
FCS:
Malte Wachsmuth
Frank Sieckmann (Leica)
Zeiss LSM780 automation:
Gwen Rabut, Annelie Wuensche, Antonio Politi
Jan Ellenberg
Rainer Pepperkok
Green: actin cytoskeleton
Red: nucleus
Cells treated with PDGF

## Slide 38: Adaptive Feedback Microscopy using ZEISS products
Microscope Examples | Zeiss Software | Open Application Development Modality | Image Analysis Modalities
LSM510 confocal (1) LSM780 confocal LSM880 confocal | ZEN Black | Visual Basic scripting with macro recording | Visual Basic or external software
LSM800 confocal CellDiscoverer 7 widefield | ZEN Blue | Python scripting with macro recording | ZEN Blue interal image analysis or external software
(1) Rabut and Ellenberg, Automatic real-time three-dimensional cell tracking by fluorescence microscopy. J. Microscopy, 2004